## Slide 1: Designing Network Security and Privacy Mechanisms: How Game Theory Can Help
Jean-Pierre Hubaux
EPFL
With contributions (notably) from
J. Freudiger, H. Manshaei, P. Papadimitratos, M. Poturalski, and M. Raya
GameSec 2010

## Slide 2: Wireless Networks
Many deployment scenarios
Spectrum is a scarce resource  Potential strategic behavior of individual devices or network operators
Paradise for game theorists ?

## Slide 3: Modern Mobile Phones
iPhone
Quad band GSM
(850, 900, 1800, 1900 MHz)
GPRS/EDGE/HSDPA
Tri band UMTS/HSDPA
(850, 1900, 2100 MHz) Soon LTE
GPS + accelerometers
WiFi (802.11b/g)
Bluetooth
P2P wireless
Nokia: NIC
Qualcomm: Flashlinq
WiFi-Alliance: Wi-Fi Direct
Notes: 3

## Slide 4: Wireless Enabled Devices
Notes: 4

## Slide 5: Satellite Communications
BTCC-45 Bluetooth GPS Receiver
Global Positioning System (GPS)
Orbit altitude: approx. 20,200 km
Frequency: 1575.42 MHz (L1)
Bit-rate: 50 bps
CDMA
Iridium 9505A Satellite Phone
Iridium Satellite
Supports 1100 concurrent phone calls
Orbit altitude: approx. 780 km
Frequency band: 1616-1626.5 MHz
Rate: 25 kBd
FDMA/TDMA
Notes: 5

## Slide 6: Wireless “Last Mile”: WiMax
WiMAX GP3500-12 omnidirectional antenna
Frequency band: 3400-3600 MHz
Gain: 12 dBi
Impendence: 50 
Power rating: 10 Watt
Vertical beam width: 10
WiMAX PA3500-18 directional antenna
Frequency band: 3200-3800 MHz
Gain: 12 dBi
Impendence: 50 
Power rating: 10 Watt
Vertical beamwidth: 17
Horizontal beamwidth: 20
Notes: 6

## Slide 7: Wireless Sensors
IEEE 802.15.4 Chipcon Wireless Transceiver
Frequency band: 2.4 to 2.4835 GHz
Data rate: 250 kbps
RF power: -24 dBm to 0 dBm
Receive Sensitivity: -90 dBm (min), -94 dBm (typ)
Range (onboard antenna): 50m indoors / 125m outdoors
TelosB Sensor Mote
MicaZ
Imote2
Iris Mote
Cricket Mote
Notes: 7

## Slide 8: Radio-Frequency Identification (RFID)
RFID tag
SDI 010 RFID Reader
ISO14443-A and B (13.56 MHz)
Operating distance: 1cm
Communication speed: up to 848 Kbit/s
Notes: 8

## Slide 9: Medical Implants
Implantable Cardioverter Defibrillator (ICD)
Operating frequency: 175kHz
Range: a few centimeters
Medical Implant Communication Service (MICS)
Frequency band: 402-405 MHz
Maximum transmit power (EIRP): 25 microwatt
Range: a few meters
Notes: 9

## Slide 10: Software Defined Radio
Tuning Frequency:
30KHz - 30MHz (continuous)
Tuning Steps:
1/5/10/50/100/500Hz & 1/5/9/10KHz
Antenna Jacket / Impedance:
BNC-socket / 50Ohms
Max. Allowed Antenna Level :
+10dBm typ. / saturation at -15dBm typ.
Noise Floor (0.15-30MHz BW 2.3KHz):
Standard: < -131dBm (0.06μV) typ.
HighIP: < -119dBm (0.25μV) typ.
Frequency Stability (15min. warm-up
period):
+/- 1ppm typ.
Application: Cognitive Radios  Dynamic Spectrum Access
Notes: 10

## Slide 11: Vehicular Communications
Dedicated short-range communications (DSRC)
Frequency band (US): 5.850 to 5.925 GHz
Data rate: 6 to 27 Mbps
Range: up to 1000m
Notes: 11

## Slide 12: Question
Would you model wireless devices / network operators by cooperative or non-cooperative games?
Back to the fundamentals…

## Slide 13: (Non)-Cooperative behavior in wireless networks: bonobos Vs chimps
Bonobo
Chimpanzee
www.ncbi.nlm.nih.gov
www.bio.davidson.edu

## Slide 14: Living places (very simplified)
Bonobos
Chimps
Congo river

## Slide 15: Cross-layer design…
Bonobos
Chimps
Congo river
Upper layers (MAC and above)
Physical layer
Cooperative
Non-
Cooperative
(or “selfish”)

## Slide 16: Cooperation between wireless devices (at the physical layer)
S
R
D
Cooperative relaying
Cooperative beamforming
D
S

## Slide 17: Non-cooperation between wireless devices (MAC and network layer)
Well-behaved node
Cheater
Well-behaved node
At the MAC layer
At the network layer
X
Note: sometimes non-cooperation is assumed at the physical layer; likewise, cooperation is sometimes assumed at the upper layers

## Slide 18: (Non-)cooperation between wireless networks: cellular operators in shared spectrum
X

## Slide 19: More on primatology

## Slide 20: Dynamic Spectrum Allocation
Rationale: wireless devices becoming very sophisticated  ``Command and Control´´ allocation of the spectrum obsolete  Less regulation !!!
Each device / each operator is a selfish agent
The market determines (in real time) the best usage of the spectrum
Already a modest realization in the ISM band (for WiFi)
IEEE DySPAN: Dynamic Spectrum Access Networks
But isn’t this rather lawyers’ paradise?
Skepticism of regulators

## Slide 21: Vulnerabilities of Wireless Devices…
… to malicious behavior
… and to selfish behavior
A Heart Device Is Found
Vulnerable to Hacker Attacks
Example in the Internet: viruses
Example in the Internet: spam
Power games in shared spectrum
(or between cognitive radios)

## Slide 22: Malice Vs Selfishness
Security/crypto
  Manichean world
  Some parties are trusted, some not
  Attacker’s behavior is arbitrary
  Attacker’s model (e.g., Dolev-Yao)
  Strength of the attacker
Game theory
  All players are selfish
  Payoff / Utility function
  Strategy space
  Information
  Agreements
  Solution of the game
  Mechanism design

## Slide 23: Who is malicious? Who is selfish?
There is no watertight boundary between malice and selfishness
 Both security and game theory approaches can be useful
Harm everyone: viruses,…
Selective harm: DoS,…
Spammer
Cyber-gangster:
phishing attacks,
trojan horses,…
Big brother
Greedy operator
Selfish mobile station

## Slide 24: Game Theory Applied to Security Problems
Security of Physical and MAC Layers
Anonymity and Privacy
Intrusion Detection Systems
Security Mechanisms
Cryptography
…

## Slide 25: Security of Physical and MAC Layers
Y.E. Sagduyu, R. Berry, A. Ephremides, “MAC games for distributed wireless network security with incomplete information of selfish and malicious user types,” GameNets 2009.
M
S
S
W
W
Players (Ad hoc or Infrastructure mode):
Well-behaved (W) wireless modes
Selfish (S) - higher access probability
Malicious (M) - jams other nodes (DoS)
Objective: Find the optimum strategy against M and S nodes
Reward and Cost: Throughput and Energy
Game model: A power-controlled MAC game solved for
Bayesian Nash equilibrium
Game results: Introduce Bayesian learning mechanism
to update the type belief in repeated games
Optimal defense mechanisms against denial of service attacks in wireless networks

## Slide 26: Economics of Anonymity
Rationale: decentralized anonymity infrastructures still not in wide use today
In the proposed model, an agent can decide to:
  act as a simple user (sending her own traffic + possibly dummy traffic)
  act as a node (receiving and forwarding traffic, keeping messages secret, and possibly creating dummy traffic)
  send messages through conventional, non-anonymous channels
Model as a repeated-game, simultaneous-move game
Global passive adversary
A. Acquisti, R. Dingeldine, P. Syverson. On the economics of anonymity. FC 2003
T. Ngan, R. Dingledine, D. Wallach. Building incentives into Tor. FC2010
N. Zhang et al. gPath: a game-theoretic path selection algrithm to prtect Tor’s anonymity GameSec 2010
Mix-net
Traffic to be anonymized
Agent

## Slide 27: Intrusion Detection Systems
Subsystem 1
Subsystem 2
Subsystem 3
Attacker
Players: Attacker and IDS
Strategies for attacker: which subsystem(s) to attack
Strategies for defender: how to distribute the defense mechanisms
Payoff functions: based on value of subsystems + protection effort
T. Alpcan and T. Basar, “A Game Theoretic Approach to Decision and Analysis in Network Intrusion Detection”, IEEE CDC 2003

## Slide 28: Cryptography Vs. Game Theory
Issue | Cryptography | Game Theory
Incentive | None | Payoff
Players | Totally honest/ malicious | Always rational
Punishing cheaters | Outside the model | Central part
Solution concept | Secure protocol | Equilibrium
Y. Dodis, S. Halevi, T. Rubin. A Cryptographic Solution to a Game Theoretic Problem.
Crypto 2000
See also S. Izmalkov, S. Micali, M. Lepinski. Rational Secure Computation and Ideal Mechanism Design, FOCS 2005

## Slide 29: Crypto and Game Theory
Cryptography
Game Theory
Implement GT mechanisms in a distributed fashion
Example: Mediator (in correlated equilibria)
Dodis et al., Crypto 2000
Design crypto mechanisms with rational players
Example: Rational Secret Sharing and Multi-Party Computation
Halpern and Teague, STOC 2004

## Slide 30: Design of Cryptographic Mechanisms with Rational Players: Secret Sharing
a. Share issuer
S1
Secret
S3
S2
Agent 1
Agent 2
Agent 3
b. Share distribution
Reminder on secret sharing
Agent 1
Agent 2
Agent 3
S1
S2
S3
c. Secret reconstruction
S1
S2
S3

## Slide 31: The Temptation of Selfishness in Secret Sharing
Agent 1
Agent 2
Agent 3
S1
S2
S3
Agent 1 can reconstruct the secret
Neither Agent 2 nor Agent 3 can
Model as a game:
  Player = agent
  Strategy: To deliver or not one’s share (depending on what the other players did)
  Payoff function:
    a player prefers getting the secret
    a player prefers fewer of the other get it
Impossibility result: there is no simple mechanism that would prevent this  Proposed solution: randomized mechanism

## Slide 32: Randomized Protocol (for 3, simplified)
1
2
3
c3R
c1L
c3L
c2R
c2L
c1R
d1
d3
d2
Protocol for agent 1:
Toss coin b1
Toss coin c1L
Set c1R = b1  c1L
Send c1L left, c1R right
Send d1 = b1  c3L left
Compute b1b2b3 = b1c2Rd3
If b1=b1b2b3 = 1, send share.
If received shares or detected cheating, quit. Else restart protocol with new share.
Main result: a rational agent will follow the protocol
J. Halpern and V. Teague. Rational Secret Sharing and Multi-Party Computation.
STOC 2004
Courtesy J. Halpern and V. Teague

## Slide 33: Improving Nash Equilibria (1/2)
4, 4 | 1, 5
5, 1 | 0, 0
Chicken
Chicken
Dare
Dare
3 Nash equilibria: (D, C), (C, D), (½ D + ½ C, ½ C+ ½ D)
Payoffs: [5, 1] [1, 5] [5/2, 5/2]
The payoff [4, 4] cannot be achieved without a binding contract, because it is not an equilibrium
Possible improvement 1: communication
Toss a fair coin  if Head, play (C, D); if Tail, play (D, C)  average payoff = [3, 3]
Y. Dodis, S. Halevi, and T. Rabin. A Cryptographic solution to a game theoretic problem, Crypto 2000
Player 1
Player 2

## Slide 34: Improving Nash Equilibria (2/2)
Possible improvement 2: Mediator
Introduce an objective chance mechanism: choose V1, V2, or V3 with probability 1/3 each. Then:
Player 1 is told whether or not V1 was chosen and nothing else
Player 2 is told whether or not V3 was chosen and nothing else
If informed that V1 was chosen, Player 1 plays D, otherwise C
If informed that V3 was chosen, Player 2 plays D, otherwise C
This is a correlated equilibrium, with payoff [3 1/3, 3 1/3]
It assigns probability 1/3 to (C, C), (C, D), and (D, C) and 0 to (D, D)
How to replace the mediator by a crypto protocol: see Dodis et al.
4, 4 | 1, 5
5, 1 | 0, 0
Chicken
Chicken
Dare
Dare
Player 1
Player 2

## Slide 35: An Example of Security (or rather, Privacy) Mechanism Modeled by Game Theory: Cooperative Change of Pseudonyms in Mix Zones
J. Freudiger, H. Manshaei, JP Hubaux, D. Parkes
On Non-Cooperative Location Privacy: A Game-Theoretic Analysis

## Slide 36: Location Privacy with Mix Zones
Mix zone
1
2
1
2
1
a
b
?
Notes: Notion of cooperation

## Slide 37: “Costs” generated by Mix Zones
Turn off transceiver
Routing is difficult
Load authenticated pseudonyms
+
+
=

## Slide 38: Sequence of Pseudonym Change Games
5
6
E2
2
3
4
E1
7
8
9
E3
1
E2
E1
E3
ui
Ai(t1)- γ
Ai(t2)- γ
γ

## Slide 39: Non-Cooperative Behavior
Benefit B of mix zone:
  Location Privacy
Strategies
  Cooperate: Change identifier in the mix zone
  Defect: Do not change
  Depend on current level of location privacy of nodes
Cost C of mix zone :
  Mobiles must remain silent
  Mobiles must change their identifier
Cooperate
Cooperate
Defect
Defect
-C, 0
B-C, B-C
0, 0
0, -C
Node 1
Node 2
Pseudonym Change Game
Notes: Assuming move in network and dynamic internal state
Misaligned incentives

## Slide 40: Nash Equilibria
The pseudonym change game is a coordination game
  Mutual gain by making mutually consistent decisions
Theorem:
The pseudonym change game with complete information has 2 pure strategy Nash equilibria and 1 mixed-strategy Nash equilibrium.  Cooperation cannot be taken for granted
= pure NE
= mixed NE
= Pr(node i cooperates)

## Slide 41: Overall Conclusion
Upcoming (wireless) networks bring formidable challenges in terms of malicious and selfish behaviors (including at the physical layer)
Game theoretic modeling of security mechanisms can help predicting and influencing (by mechanism design) the behavior of the involved parties
A lot of work still needs to be accomplished to establish the credibility of such approaches
http://lca.epfl.ch/gamesec
H. Manshaei, Q. Zhu, T. Alpcan, T. Basar, JP Hubaux
Game Theory Meets Network Security and Privacy
EPFL Tech Report 151965 , Sept. 2010